## Slide 1: Number System

## Slide 2: Common number systems
System | Base | Symbols | Used by humans? | Used in computers? | Used by Forensic Professionals?
Decimal | 10 | 0, 1, … 9 | Yes | No | Yes
Binary | 2 | 0, 1 | No | Yes | Yes
Hexa- decimal | 16 | 0, 1, … 9, A, B, … F | No | No | Yes

## Slide 3: Conversion among number systems
Hexadecimal
Decimal
Binary

## Slide 4: Conversion
Decimal | Binary | Hexa- decimal
0 | 0 | 0
1 | 1 | 1
2 | 10 | 2
3 | 11 | 3
4 | 100 | 4
5 | 101 | 5
6 | 110 | 6
7 | 111 | 7
Decimal | Binary | Hexa- decimal
8 | 1000 | 8
9 | 1001 | 9
10 | 1010 | A
11 | 1011 | B
12 | 1100 | C
13 | 1101 | D
14 | 1110 | E
15 | 1111 | F

## Slide 5: Decimal to Decimal
12610 => 6 x 100 = 6 2 x 101 = 20 1 x 102 = 100 126
Base
Weight
placeholder
Decimal

## Slide 6: Binary to Decimal
Multiply each bit by 2n, where n is the “weight” of the bit
The weight is the position of the bit, starting from 0 on the right
Add the results
1010102 => 0 x 20 = 0 1 x 21 = 2 0 x 22 = 0 1 x 23 = 8 0 x 24 = 0 1 x 25 = 32
4210
Bit “0”
Base
Weight

## Slide 7: Hexadecimal to Decimal
Multiply each bit by 16n, where n is the “weight” of the bit
The weight is the position of the bit, starting from 0 on the right
Add the results
AB216 =>
2 x 160 = 2 x 1 = 2 B x 161 = 11 x 16 = 176 A x 162 = 10 x 256 = 2560
273810

## Slide 8: Decimal to Binary
Divide by 2, keep track of the remainder
First remainder is bit 0 (LSB, least-significant bit)
Second remainder is bit 1
Etc.
2 126 63 0
2 31 1
2 15 1
2 7 1
2 3 1
2 1 1
2 0 1
12610 = 11111102
stop
12610 = ?2

## Slide 9: Decimal to Hexadecimal
Divide by 16
Keep track of the remainder
16 2738
171 2
16
10 11 = B
16
0 10 = A
273810 = AB216
273810 = ?16

## Slide 10: Binary to Hexadecimal
Group bits in fours, starting on right
Convert to hexadecimal digits
1010101100102 = ?16
1010 1011 0010
10 11 2
A B 2
1010101100102 = AB216

## Slide 11: Binary Addition
A | B | A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 10
carry bit
10101 21 + 11001 + 25 101110 46
1
1

## Slide 12: Bit, Byte
A ‘bit’ (from Binary + digIT)
  is the smallest unit of memory,
  the unit of measurement of data information.
Byte 8-bit collections
  A single bit holds so little information.

## Slide 13: Endianness
Endianness is a term that describe the order in which a sequence of bytes is stored in memory.
Big-endian
  is an order in which the "big end" (most significant value in the sequence) is stored first (at the lowest storage address).
Little-endian
  is an order in which the "little end" (least significant value in the sequence) is stored first.

## Slide 14
https://www.iar.com/knowledge/learn/programming/migration-techniques-for-different-endianness/

## Slide 15: ASCII - American Standard Code for Information Interchange
ASCII codes represent text in computing devices.